## Slide 1: An overview of the CS-2 architecture

## Slide 2: We have a (fairly big) box
This contains all the cooling and infrastructure support
  15RU and draws around 23kW of power
Uses standards-based power and network connections
  12x standard 100 Gigabit Ethernet links and converts standard TCP-IP traffic into Cerebras protocol at full line rate
This all serves the Cerebras Wafer Scale Engine (WSE)
  A wafer-parallel compute accelerator, containing hundreds of thousands of independent processing elements (PEs)
  The WSE is the reason for the tutorial!

## Slide 3: Cerebras Wafer Scale Engine (WSE)
Physically it is about as big as a dinner plate and built upon a 7nm process technology
The current generation CS-2 that we will use today contains:
  Approximately 850,000 cores
  40GB on-chip SRAM memory
  A total of 20PB/s aggregate memory bandwidth
The flexibility of the individual, independent cores and the large amount of memory means that, depending on the workload, the CS-2 is capable of delivering the performance of many GPUs
  Although of course this depends heavily on you programming it effectively, which is the topic of the tutorial today!

## Slide 4: WSE conceptual high-level view
Very many individual Processing Elements (PEs)
  These run independent of each other (e.g. their own program counter)
PEs are connected by 2D rectangular mesh across the chip
  32-bit messages (called wavelets) can be communicated with neighbours in a single cycle
The 40GB of WSE memory is distributed amongst the PEs
  Each PE has its own private chunk of memory

## Slide 5: Within each Processing Element (PE)
We have the processor itself
  Commonly referred to as the Compute Engine (CE)
  Independent and private from any other
A router
  Connected with bidirectional links to own CE and router of four neighbours
  Link to own CE is called the RAMP and neighbours are referred to by north, south, east and west
  This is the only way in which PEs can communicate
Local (private) memory
  All data and code for the PE is stored in this memory
  48KB per PE

## Slide 6: How this is driven
Driven by a host program which is written in Python using the Cerebras API
Copy your device program onto applicable PEs of CS-2
Copy any input data onto the CS-2
Run the code on the CS-2
Once completed, copy any results back
Host
Cerebras CS-2
On the WSE itself, data is communicated to/from the array via edge connectors, the hardware and Cerebras SDK abstracts getting data to/from the individual PEs

## Slide 7: Programming the WSE
Cerebras Software Language (CSL) is used to actually program the device
  As we will see, this provides both a series of abstractions for high level programming with the ability to get down into the low level details (the same level as C) if desired
var result: f32 = 0.0;
task main_task() void {
result = 5.0;
}
CSL program consists of tasks and functions
  Functions can be called by the host or another function on the device
  Tasks are started by the hardware, run until completion, and then at that point the hardware chooses another task to run
    Can only be activated, can not be called by other tasks or functions. Also don’t return a value
    Each task has an associated ID that is used for tracking and management

## Slide 8: Communication between PEs
Remember, a wavelet is a 32-bit message communicated with a neighbour in a single cycle
Each physical channel has 24 virtual communication channels known as colours that can be used for passing wavelets
Each wavelet has associated with it a 5-bit identify which defines which channel it is communicated on
  Determines the wavelet’s routing through the fabric and its consumption
  This is a bit like a tag in MPI point-to-point communications, and similarly many messages on one colour does not block messages with a different colour using the same physical link
Wavelets are consumed by tasks on a PE where a task is registered to execute when a wavelet arrives with a specific colour

## Slide 9: Three types of task
Data tasks
  Which activate upon the arrival of a wavelet with a matching colour, these are used to consume messages that are communicated between PEs
  Wavelet Triggered Task (WTT)
Local tasks
  Explicitly activated by other tasks or functions running on the PE
Control tasks
  Can be either data or local tasks, or neither (we will see examples later on)

## Slide 10: Host runtime
A host-side runtime known as SdkRuntime is provided
  memcpy library loads programs, launches functions, and transfers data on and off the WSE
  Functions provided by SdkRuntime manage the data transfer to and from the host’s filesystem or memory
  The host and WSE network interfaces finally route the data into your kernel (last step is implemented on the WSE itself to connect the I/O channel entry-points, which are in fixed locations at the edges of the WSE, to each kernel, which has a variable size and location.)
  memcpy infrastructure uses additional PEs around the user kernel to route tensor data and also adds a small executable component to the kernel PEs. In addition to a halo around the kernel, the additional support PEs consume three columns on the West of the kernel and two columns on the East.

## Slide 11: The CSL compiler
Code is compiled using the cslc command
Generates a .elf file which is the executable that will be loaded onto the CS-2
Will play with this in a few minutes
usage: cslc [-h] [-o OUTPUT_NAME] [--params PARAMS] [--colors COLORS] [--memcpy] [--channels CHANNELS]
[--import-path IMPORT_PATH] [--width-west-buf WIDTH_WEST_BUF] [--width-east-buf WIDTH_EAST_BUF] [--verbose]
csl_filename
Frontend for cslc-driver. Creates a directory and then calls cslc-driver which will write its output files to the created directory.
positional arguments:
csl_filename Input CSL file
optional arguments:
-h, --help Show this help message and exit
-o OUTPUT_NAME Output directory name (default: out)
--params PARAMS Comma-separated list of param-to-value mappings where a mapping is a `name:value` pair where name
is a string and value is an unsigned integer. The parameter list is passed on to cslc-driver as-is.
--colors COLORS Comma-separated list of color-to-value mappings where a mapping is a `color:value` pair where color
is a string and value is an unsigned integer. The parameter list is passed on to cslc-driver as-is.
--memcpy Add memcpy support to this program
--channels CHANNELS Number of memcpy I/O channels to use when memcpy support is compiled with this program.
--import-path IMPORT_PATH
Add the given directory to the list of directories searched for <...> paths in @import_module and
@set_tile_code statements.
--width-west-buf WIDTH_WEST_BUF
Width of west buffer (default is zero, i.e. no buffer to mitigate slow input)
--width-east-buf WIDTH_EAST_BUF
Width of east buffer (default is zero, i.e. no buffer to mitigate slow output)
--verbose Verbose output

## Slide 12: Use of the simulator
CS-2 machines are designed to be exclusive use
  Routinely developing code directly on the CS-2 would be a big pain, due to contending with lots of other users at the same time!
Cerebras also provide a software simulator of the CS-2
  Simulates execution of your program by running it on the CPU
  This is highly accurate and should be used during development to test your code
  But for performance measurements and production runs obviously we need the CS-2 itself
We will use the simulator quite heavily during this tutorial
  But part of our hands-on exercises will be to run each of these on the CS-2 hardware itself once you have done the development

## Slide 13: Clustering CS-2 machines
It’s possible to combine CS-2 machines together to provide a very large virtual CS-2
We will not cover this in the tutorial today, but details are available on the Cerebras website

## Slide 14: Conclusions